## Slide 1: DOE Final Project
By Michael Giannattasio

## Slide 2: Research Question
How to minimize patient staytime with different layouts and staffing counts?

## Slide 3: Experimental Methodology
Tackling the problem using a factorial design

## Slide 4: Why Factorial Designs (Why 2^k)?
Results of layout optimality for patient care are usually analyzed in 1-D settings
  i.e. Which layout is better?
Does not analyze potential interaction effects with staffing
  Resource availability and bottlenecking
  Travel time importance discrepancies
Full factorial design allows for total comprehensive understanding of higher-level interactions
  Provides more complete, real-world applicable recommendation
2^k Design
  Factor screening
  High number of factors considered while manageable data maintained
  Allows for replicates (4 is adequate)

## Slide 5: Literature Inspiration:
Wan, Hong, and Bruce E. Ankenman. "Two-stage controlled fractional factorial screening for simulation experiments." Journal of Quality Technology 39.2 (2007): 126-139.
Presents structure for fractional factorial designs with simulation and potential drawbacks
Overviews benefits of using simulations
Price, Time, Ease of Altering Factor Levels
Outlined methods for simulation combined with 2^k design to optimize clinical intervention
Averill M. Law. 2014. A tutorial on design of experiments for simulation modeling. In Proceedings of the 2014 Winter Simulation Conference (WSC '14). IEEE Press, 66–80.
Tutorial on combining DOE and DES
Kuhn, J., Sheldrick, R.C., Broder-Fingert, S. et al. Simulation and minimization: technical advances for factorial experiments designed to optimize clinical interventions. BMC Med Res Methodol 19, 239 (2019). https://doi.org/10.1186/s12874-019-0883-9

## Slide 6: Literature Inspiration:
S. M. Sanchez, "Work Smarter, not Harder: Guidelines for Designing Simulation Experiments," Proceedings of the 2006 Winter Simulation Conference, Monterey, CA, USA, 2006, pp. 47-57, doi: 10.1109/WSC.2006.323037.
Gives best practices for intelligent design of a simulation for factorial experiments
R. C. H. Cheng and O. D. Jones, "Analysis of simulation factorial experiments by EDF resample statistics," 2000 Winter Simulation Conference Proceedings (Cat. No.00CH37165), Orlando, FL, USA, 2000, pp. 697-703 vol.1, doi: 10.1109/WSC.2000.899782.
Gives outline for using EDF statistics instead of ANOVA for nonnormally-distributed simulation results

## Slide 7: Feasibility of Experiment
How to implement this factorial design?

## Slide 8: Benefit of Simulation
Allows for hypothetical layout construction
Experimental validity:
  Allows for randomness and near-normality:
    Long runtimes
    High replicates
    Large Factor Levels
    Automatic implementation
Cost- and Time- Effective
No significant ethical issues

## Slide 9: Benefit of Simulation
Basically, only feasible with simulation
With FlexSim, the desired experimental structure is possible!

## Slide 10: Data Collection

## Slide 11: Two Hospital Layouts

## Slide 12: Parameter/Performance Measure Setup

## Slide 13: Experimenter Configuration

## Slide 14: Experimenter Configuration
2^5 Factorial design chosen
  Factor Screening
  Consistent with Literature
  Allows for reasonable data collection with replicates
Minitab/FlexSim both randomize data collection

## Slide 15: Data Sanitization:
Data sanitized in Excel

## Slide 16: Statistical Analysis

## Slide 17: Model Assumptions:

## Slide 18: Original Model Results

## Slide 19: Reduced Model Results
Note:
  Insignificant D (Right RNs) is maintained to keep model hierarchical
  Adjusted and Predictive R-squared both increased

## Slide 20: Factorial Plots & Results
Goal is to reduce staytime (minimzation)

## Slide 21: Context-based Results
Despite optimization giving the best solution above
A cost-benefit analysis is important
  L/RRNs treatment effects are not significant
  RNs are incredibly expensive
  Visualization shows no variability changes
  "Optimal" values are 3

## Slide 22: Implications
RMDs seem to be the system bottleneck in both systems
  Largest effect size
Followed by layout then LMDs
  Layout with proximity leads to lower patient staytimes
Significant interactions present
  Layout and LMDs
  LMDs and RMDs
  RRNs and RMDs

## Slide 23: Implications
While layout –1 had a significant reduction of staytime:
New layout should be designed to
  Minimize MD travel time
  Even at expense of RN travel time
Emphasis should be placed on MDs instead of RNs
  Training to reduce process duration
  Potential new hiring of staff

## Slide 24: Drawbacks to Experimental Design
Only analyzed a limited number of operating factors
However, factor screening showed which are significant
Could be replicated without RNs, but with other procedural adjustment factors
Limited number of replicates
Still normality in data
Want to scale this up for validity in final advisement
Fractional factorial can be used to analyze effects with large data size
Limited number of layouts presented

## Slide 25: Thanks for Listening!
And a special thanks to Arhum Shaikh for his contributions!

## Slide 26: References
Wan, Hong, and Bruce E. Ankenman. "Two-stage controlled fractional factorial screening for simulation experiments." Journal of Quality Technology 39.2 (2007): 126-139.
Averill M. Law. 2014. A tutorial on design of experiments for simulation modeling. In Proceedings of the 2014 Winter Simulation Conference (WSC '14). IEEE Press, 66–80.
Kuhn, J., Sheldrick, R.C., Broder-Fingert, S. et al. Simulation and minimization: technical advances for factorial experiments designed to optimize clinical interventions. BMC Med Res Methodol 19, 239 (2019). https://doi.org/10.1186/s12874-019-0883-9
S. M. Sanchez, "Work Smarter, not Harder: Guidelines for Designing Simulation Experiments," Proceedings of the 2006 Winter Simulation Conference, Monterey, CA, USA, 2006, pp. 47-57, doi: 10.1109/WSC.2006.323037.
R. C. H. Cheng and O. D. Jones, "Analysis of simulation factorial experiments by EDF resample statistics," 2000 Winter Simulation Conference Proceedings (Cat. No.00CH37165), Orlando, FL, USA, 2000, pp. 697-703 vol.1, doi: 10.1109/WSC.2000.899782.